## Slide 1: Catia design tables
20° and 14.5° Pressure angle gears

## Slide 2: 20° Pressure angle Gears

## Slide 3: 20° Pressure angle Gears
Issues encountered
Incorrect Associations
  Despite assuring that dimensions in CATIA match Column headers manual association is required.
Dimensions in inches (“)
  At first I removed the inch (“) from design table, resulting in exploded part, maintain (“) in table.
3-Decimal Maximum
  Converting fractions to decimals resulted in 4 decimal places in Excel, had to round to 3 decimals for CATIA requirement.

## Slide 4: 20° Pressure angle Gears
Initial Sketches
  The initial sketches were easily produced as they were initial built from a McMaster-Carr Part Drawing.
Named Dimensions
  After creating the dimensions I named them specific and identifiable names in their properties so that I could easily associate them to the design table later.
Design Process

## Slide 5: 20° Pressure angle Gears
Design Process
Gear Formulas
  Modeling Involute gears is very difficult, using equations from Cameron Stefanic’s Masters thesis I was able to create simplified formulas to generate gear shapes.

## Slide 6: 20° Pressure angle Gears
Gear Sketches
  The sketch of the gear teeth is determined from the previous formulas allowing for the design table to change key dimensions and update all aspects of the teeth.
Design Process

## Slide 7: 20° Pressure angle Gears
Final Designs

## Slide 8: 14.5° Pressure angle Gears
Issues encountered
Gear Teeth Drawing
  The change of the gear angle broke the relations of the teeth geometry, updated sketch to include curved radius to match McMaster-Carr

## Slide 9: 14.5° Pressure angle Gears
Final Designs