ME529 Combustion and Air Pollution – HW#4 - Excess Air, Flue Gas Analysis, Properties, LHV and HHV, Heat of Reaction, Adiabatic Flame Temperature

- The higher heating value for a bluegrass straw is posted on the Mindworks site.
Calculate the lower heating value for this sample…

  - on an as-received basis

  - on a dray basis

- What is the percentage excess air when the propane is combusted in air at an equivalence ratio of 0.75?

- Problem 2.22 LHV and HHV.  Compare your results with Appendix B.1.

- Review the handout about ‘endo gas’ used in a heat treat furnace.

  - Determine the mole fraction of each constituent of the reactants and products.

  - Determine the mass fraction of each constituent of the reactants and products.

  - Determine the molecular weight of the reactant and product mixtures.

  - Calculate and plot the heat of reaction from 30C to 1200 C, assuming that reactants are at 30 C.

  - Estimate how many cubic feet of natural gas are required to produce a cubic foot of endo gas.

- Using the data in Appendix A, calculate the adiabatic constant-pressure flame temperature for a boiler operating with the fuel blend and equivalence ratio given in Problem 2.17.  Assume complete combustion to CO2 and H2O and neglect any dissociation.  The boiler operates at 1 atm, and both the air and fuel enter at 298 K.