## Slide 1: Ethanol Compensation
Presented by:
Davis hill

## Slide 2: Outline
What is it?
Why do we Care?
Measuring Ethanol Content
Flex Fuel Circuit
Wiring
Homework
Questions

## Slide 3: What is it?
What does the US Produce?
  Freedom
  Corn
Corn Facts:
  The US is the leading grower of corn in the world (obviously)
  Corn was first found in Mexico
  In 2013 the US produced 13 BILLION bushels of corn
  8% is consumed by the world population
  40% goes into Biofuels (ETHANOL!!)

## Slide 4: Why do we care?
Ethanol Pros
  Burns Cleaner (fewer aldehydes, CO, and )
  Higher Energy Content (~105 Octane)
CSC Rules
  Requires all sleds to be “Flex Fuel Capable”
  0-85% ethanol content
  Exact amount unknown

## Slide 5: Our unit
Zietronix Flex Fuel
Replaces Intake Air Temp input to ECU
Recalibrated the ECU for ethanol compensation
Module on Spectre
Actual sensor

## Slide 6: Measuring Ethanol Content
How the sensor works
Sends an AC Voltage
Measures Capacitance of Fuel (related to change in voltage)
Outputs a oscillatory voltage response (sine wave) at signal wire
Frequency of output is proportional to ethanol %
Sine wave converted to steady voltage via the Flex Fuel Circuit

## Slide 7: Flex Fuel circuit
Circuit calibration
Step 1:
  Know the voltage range for ethanol
Step 2:
  Calibrate Extremes (E00 & E85)
Step 3:
  Linearly Interpolate injection quantity
  in calibration of EMM
Chart: INPUT
Chart: Output
Zietronix Box
Z
Ethanol content %
Injection quantity
E0
E85

## Slide 8: Wiring
Block diagram
Flex Fuel Sensor
Module
ECU
Air Temp Sensor
ECU
Stock
CSC modified

## Slide 9: Wiring
General Wiring diagram
Z

## Slide 10: Homework

## Slide 11: Questions?

## Slide 12: Old circuit
Circuit inputs
Continental sensor used to measure volume fractions of ethanol
In-house designed circuit (2012 Senior Design)
  Lovingly referred to as the orange box
  Unchanged since Senior Design Project