## Slide 1: ME 433 Internal Combustion Engines
Professor:
Dr. Dan Cordon (AKA Dr. Dan)

## Slide 2
Road Load Modeling
Drag Force (aerodynamics)
θ
Weight (gravity)
Rolling Resistance (tires/bearings)
Propulsion Force (from engine/motor)
We can use Equations of Motion (EOM) to model the steady-state power requirements or transient response of a vehicle.
The key forces acting on a road-going vehicle are depicted in the figure below.

## Slide 3
Σ Forces against Direction of Travel
Drag Force
Theta
θ
height
distance
Rolling Force
Gravity Force

## Slide 4
Typical Values
Drag Force
For most vehicle shapes the coefficient of drag is:
0.3 < cD < 0.5
Rolling Force
For most rubber-tire vehicles the coefficient of rolling resistance is:
0.008 < cR < 0.035
Frontal Area
Bicycle and Rider 0.3 – 0.5 [m2]
Motorcycle and Rider 0.5 – 0.8 [m2]
Small Car 1.6 – 2.0 [m2]
Typical Sedan 2.0 – 2.5 [m2]
Typical SUV 2.7 – 3.5 [m2]
Semi Truck ~9.5 [m2]

## Slide 5
Power
Required Road Power (steady-state)
Calculate
Toyota Supra on Flat Ground
AF = 2.23 [m2]
cD = 0.38 and cR = 0.01
Weight = 3415 lbf = 15,190 [N]
Rhoair = 1.2 [kg/m3]
Speed = 35 [mph] = 15.7 [m/s]
Theta = 0
Calculate
Honda Accord on Lewiston Grade
AF = 1.86 [m2]
cD = 0.32 and cR = 0.008
Weight = 3000 lbf = 13,345 [N]
Rhoair = 1.2 [kg/m3]
Speed = 65 [mph] = 29.1 [m/s]
Theta = 3.7 [deg]

## Slide 6
Σ Forces = m*a
Acceleration Model
If you have a Torque and Speed at the engine you’re just a few steps away from having a Force and Velocity at the wheels.
Remember that for geartrains the gear ratio (either the radius ratio or number of teeth ratio) will act as a torque multiplier and a speed reducer.
The velocity of the tire-road interface can be related to the tire radius and RPM of the tire.

## Slide 7
Week 8 Homework
You get to choose a vehicle that you are going to virtually install the engine you’ve been modeling the last few weeks.
For this vehicle, plot Road Load vs. velocity
Based on peak power and a drivetrain loss, calculate maximum theoretical top speed for that combination.
Using data about Torque vs. RPM for your engine, and the various gear ratios in the transmission and differential make a propulsion force vs. vehicle speed plot for all gears of the transmission.
Make a simulation (Excel, Matlab, EES, python, etc.) that predicts the 0-60 mph acceleration of your virtual vehicle.
  Can use Euler’s Method (small time steps) to find change in velocity.
  Can incorporate tire traction limitations if you want.
  If your vehicle has to shift gears, include a time with zero propulsion force (0.125 to 0.5 seconds) while shifting.