Moment 		Of 		Inertia

| MOI's |  | Principal MOI's |  |
| --- | --- | --- | --- |
| Iy | 26.6835 | I1 | 102.09 |
| Ix | 99.64 | I2 | 24.23 |
| Ixy | -13.59 |  |  |

| Element | b | h | Ai | x | y | Ai x | Ai y | x' | y' | Ai x' | Ai y' | Ai x'2 | Iy0 | Ai y'2 | Ix0 | Ai x'y' |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | 6 | 1 | 6 | 3 | 6.5 | 18 | 39 | -0.27 | 2.37 | -1.62 | 14.2 | 0.4374 | 18.0 | 34 | 0.500 | -3.8394 |
| 2 | 1 | 5 | 5 | 3 | 3.5 | 15 | 17.5 | -0.27 | -0.63 | -1.35 | -3.2 | 0.3645 | 0.417 | 2 | 10.4 | 0.8505 |
| 3 | 4 | 1 | 4 | 4 | 0.5 | 16 | 2 | 0.73 | -3.63 | 2.92 | -14.5 | 2.1316 | 5.33 | 53 | 0.333 | -10.5996 |
| Sum |  |  | 15 |  |  | 49 | 58.5 |  |  | -0.05 | -3.45 | 2.9335 | 23.75 | 88.3935 | 11.25 | -13.5885 |

# Text boxes

- Divide the cross-sectional area into elements.  Cut up the cross-section into simple shapes, such as rectangles, triangles, circles, etc.

- Determine the area of each element.  After finding these, add them all together to find the total area of the shape.

- Select a convenient system of coordinate axes.  It is best if the coordinate axes lay outside of the cross-section.

- Find the centroids of each element relative to the coordinate axes.  Record distance from the centroid to the x axes as x1, and distance from the centroid to the y axes as y1.

- Find the static moment of each element.  Multiply the Area of each element with the distance from the centroid of each element to the reference axes(x and y).  Add them all together to get total static moments Aix and Aiy.

- Locate the centriod of the entire cross-section relative to the reference axes.  This is done by dividing the Aix  and Aiy by the total area.

7.	Calculate the 2nd moment of area for each element about the reference axes.  Multiply the Area of each element by the square of the distance from the centroid of each element to the centroid of the cross-section(x1 and y1).

8.	Calculate moments of Inertia of each element about it’s own centroid.  Check the basic shapes at the bottom of poster for help.

9.	 Calculate Ix and Iy.  Do this by adding the results from step 7 and 8.

10.	Calculate Ixy.  Add together the Area for each element multiplied by x1 and y1 with Ioxy for each element, and sum the results for all the elements.

11.  	Find the principal moments of inertia.  Use this equation.

Ixy=0

Ixy=0

Ixy=0

Ixy=0

n=number of sides

X

Y

1

2

3